## Slide 1
Critical Minerals Potential of Armenia:
An Overview
Samvel Hovakimyan
Institute of Geological Sciences of the Armenian National Academy of Sciences
May 16th 2026
Dilijan
«22IRF‐08» Incoming Research Fellowship Program 2022
Notes: Hello everyone,
Today I am going to provide you with an overview of critical minerals potential of Armenia. This is the project we started about three yeas ago, founded by the Sciences Committee of Armenia

## Slide 2
Increasing complexity of metal alloys in daily technologies
Braux & Christmann (2012, Géosciences n° 15)

## Slide 3
Critical minerals applications
from J.Edmondson, 2021
CRMs are used and needed in almost all industrial productions

## Slide 5
From the Seven Metals of Antiquity to…
Of the 83 stable (nonradioactive) elements,
~60 are directly embedded in your smartphone.

## Slide 6
A smartphone contains:
56 % of plastic
25 % of metals
16% of glass & ceramics
3% other
https://elements.visualcapitalist.com/
Critical minerals: They are everywhere – No metals, no connections

## Slide 8
Chart: Change in Production Since 1960
| 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011
Rare Earths | 0 | 0.62555 | 2.533 | 1.6696 | 0.62115 | 2.0661 | 6.1366 | 6.4449 | 6.1366 | 6.9736 | 6.0044 | 6.2247 | 7.0176 | 9.5727 | 10.2775 | 8.7357 | 7.6784 | 9.793 | 10.674 | 11.6872 | 11.0264 | 12.4802 | 10.7181 | 12.8326 | 17.2379 | 18.163 | 16.5771 | 19.6608 | 23.3612 | 25.7401 | 22.304 | 17.37 | 21.0705 | 19.5727 | 23.2731 | 31.7313 | 34.1101 | 29.0881 | 32.9648 | 37.1498 | 39.0441 | 40.63 | 42.2599 | 41.7753 | 43.9339 | 52.7445 | 59.3524 | 53.6256 | 55.8282 | 57.1498 | 53.185 | 47.8987
Rare
Earth
Metals

## Slide 9
Metals used in electric cars compared to conventional cars
Cu
Ni
Graphite
Co
Mn
Li
Electric car
Cu
Mn
kg / car
https://elements.visualcapitalist.com/
Conventional car
Notes: For instance, electric cars require 6 to 7 times the amount of metals compared to conventional cars
And some of the metals were not used previously in our car industry
If we want to electrify the majority of our cars in the future, a huge amount of metals needs to be supplied my mining
Mining will be intensified

## Slide 10
Challenges of the energy transition:
Expected demand growth of metals for energy production
Notes: Next to wind, solar energy is also widely implemented
Here also the growth for the demand of various metal will just be rising enormously

## Slide 11
Unequal distribution of mineral resources:
the example of Rare Earth elements
Notes: One example is the Rare Earths Elements
Indeed, China is the main producing country
With the other major suppliers way behind it

## Slide 12
Challenges of the energy transition:
Limited numbers of metal producing countries  high dependence of foreign supply of metals for batteries
Notes: Like for copper, the other main battery metals, lithium, nickel and cobalt are produced from a limited of geological environments and countries
Resources of such elements are unevenly distributed on Earth
This is also true for critical metals required for the energy transition
This can create a supply risk, with monopolies of some resources
We clearly need to diversify our sources of metals necessary for the energy transition

## Slide 13
Source: Data from the UK Critical Minerals Intelligence Centre, 2022
Top producers globally of the 18 critical minerals
Countries accounting for largest share of global supply of CRMs

## Slide 14
Critical minerals: Variable and changing classifications
https://elements.visualcapitalist.com/

## Slide 15
(Goodenough, 2022)
Different types of metallic resources

## Slide 16
Bibienne et al. (2020)
2000
2018
https://elements.visualcapitalist.com/
Challenges of the energy transition: Lithium producing countries & main use
Notes: By contrast, lithium shows how quickly the demand can grow for a specific element
Less than ten years ago lithium had a peaceful and easy going life and was used predominantly in the ceramic, glass and grease industry
Although its ideal properties for batteries was known for a long time
The sudden major growth of the battery market has resulted in an increased demand and mining for this element
Which is mainly mined in a limited number of countries, including Australia, Chile, China and Argentina.

## Slide 17
Challenges of the energy transition: Lithium deposits
https://www.mineralinfo.fr/fr/ecomine/
marche-du-lithium-2020-enjeux-paradoxes
Bowell et al.
(2020)
Salar, Andean belt
Spodumene in pegmatite
(3-4 % Li) –Zimbabwe
Notes: Basically, there are two main types of lithium deposits
A hard rocks source consists of lithium-rich pegmatites, where spodumene and other lithium-bearing minerals are mined such as in Australia, Brazil, Portugal or Zimbabwe
In many cases, such pegmatites have been mined previously for other metals such as tin
The other source are brines and salar deposits, where the Andes are a major supplier
Another source consists of lithium-rich clay minerals, especially mined in the United States
These deposits diverge in terms of ore grades and tonnage
Salar deposits having large tonnages but lower lithium grades
And pegmatite deposits having usually higher grades but lower tonnages

## Slide 18
Inside a Lithium-Ion Battery
Notes: We commonly associate electric mobility and energy storage with batteries, lithium batteries
But such batteries are not only lithium
Which is in the electrolyte moving between anode and cathode
In fact, lithium is only a minor component in such batteries
Other major components include copper, nickel, cobalt and aluminium for instance, not always perceived as critical metals.
In fact, battery metals are an ideal example for the diversity of geological environments supplying such metals, from a limited number of countries

## Slide 19
Cu
Metals come from mines
Notes: Copper a major component for the electrification of our society is a good example
The main copper production comes from South America, related to the ideal location of Chile and Peru along a major and long living subduction zone

## Slide 20
Wellmer (2012, Géosciences n° 15)
Main metals used by mankind over time

## Slide 21
Nurmi & Wilklund
(2012, Géosciences n° 15)
6,87 milliards d’habitants
Critical minerals: Growth of demand– Case of copper

## Slide 22
https://elements.visualcapitalist.com/
Challenges of the energy transition: Increasing copper demand

## Slide 23
Main copper producers
Main users of copper
Production de cuivre (% par rapport au Chile: 5’320’600 tonnes en 2005)
Challenges of the energy transition: Unequal distribution
of metal producers – The example of copper

## Slide 24
Antonio Arribas & Jeffrey Hedenquist 2020
Location of porphyry Cu-Mo and epithermal Au-Ag-Cu deposits along metallogenic belts at convergent margins
Notes: Economic significance; very relevant to a large proportion of these deposits.
Specially today, when we understand that discovering the next big porphyry or
epithermal deposits will likely involve drilling through alteration lithocaps .
To start the description of these environments let’s go to magmatichydrothermal
systems driven by shallow intrusions in arcs (transition to next
slide)

## Slide 25
Central Tethyan metallogenic belt
Moritz et al. (2021)

## Slide 26
Moritz et al., 2016
Mesozoic, related to Somkheto Karabakh island arc, and the Kapan block
Distribution of the main mineral deposits in Armenia
Cenozoic, related to subduction, collision and post collisional evolution of the Gondvana derived South Armenian Block with Eurasia
Notes: Ore deposits and prospects in Armenia are distributed along two metallogenic belts, including the Jurassic- Cretaceous Somkheto-Karabagh island-arc which is considered as the southern margin of the Eurasian plat, and the Cenozoic Gondwana derived South Armenian block, which is a microcontinent of the Arabian plate.

## Slide 27
Main targets of critical metals in Armenia
modified from Mederer et al. 2014
The Tejsar and Meghri alkaline complexes
Porphyry Cu-Mo deposits, and related mine wastes and tailings
Epithermal gold and base metal deposits, mine wastes and tailings
Cu-rich pyrite and polymetallic deposits
Pegmatite and tourmaline-bearing rocks
The Abovyan Kiruna-type IOA deposit
Mineral waters of Armenia
Notes: Critical minerals occur in diverse geological environments and mineralized systems in Armenia

## Slide 28
Southern Armenian Block: Potential for alkaline silicate REE-HFSE & Li deposits related to Cenozoic mantle-dominated & K-rich magmatism
REE-HFSE Potential ?
Meliksetian (1971); Sokoł et al. (2018); Grosjean et al. (2022)
Tejsar
REE-
HFSE
Spodumene-bearing pegmatite of the Tejsar complex
Initiation of collision to post-collision high-K magmatism
Tejsar alkaline ring complex
The Tejsar nepheline syenite complex has been identified as a major source of REEs (lanthanides, Sc, and Y) and High Field Strength Elements (HFSE) (Zr, Hf, Ti, Nb, Ta) in Armenia. Other elements that have been reported include:
0.3 wt% Li; 0.0008 wt % Be; 0.008 wt % Rb; 0.03 wt % La; 0.01 wt % Sr; 0.03 wt % Ce; 0.001 wt % Sc; 0.003 wt % Cs; 0.003 wt % Ga, 0.003 wt % Tl, and 0.001 wt % Y.
from Moritz et al. 2021
Chart: 
| La | Ce | Pr | Nd | Sm | Eu | Gd | Tb | Dy | Ho | Y | Er | Tm | Yb | Lu
Neph. Syenite | 66.396 | 38.552 | 23.2629 | 14.1068 | 6.1635 | 3.2186 | 3.1848 | 2.4612 | 2.0066 | 1.7644 | 2.0196 | 1.8283 | 1.8531 | 1.8718 | 1.8945
Neph. Syen. Pegmat. | 128.356 | 66.8893 | 33.5886 | 17.3534 | 6.7643 | 3.6412 | 3.6005 | 3.0627 | 2.8066 | 2.7911 | 3.16 | 3.1111 | 3.4079 | 3.4911 | 3.6
Neph. Syen. Pegmat. | 85.46 | 43.172 | 19.7917 | 9.2863 | 3.2281 | 1.8196 | 1.5109 | 1.2313 | 1.0659 | 0.98515 | 1.3893 | 1.064 | 1.2325 | 1.4344 | 1.5934
Neph. Syenite | 55.38 | 39.2747 | 27.6295 | 18.3945 | 9.1179 | 4.5392 | 4.6386 | 3.3925 | 2.5846 | 1.9485 | 1.8304 | 1.633 | 1.3355 | 1.1089 | 0.8967
Hambaryan (PhD thesis; in progress)
New ICP-MS analyses
Notes: The Cenozoic Tejsar alkaline ring complex is located in the central north of Armenia.
Potential of REEs and Li deposits related to the Tejsar alkaline complex
Li – bearing pegmatite in the Tejsar alkaline complex
Spodumene is found in micaceous pegmatites in the form of small nest-shaped segregations among muscovite flakes (Babadjanyan, 1970).
Polylithionite forms irregularly shaped segregations in brecciated fluorite-biotite zones, in muscovite pegmatites of the Tejsar alkaline complex.
Polylithionite is formed in the late stages of the pegmatite process due to the replacement of orthoclase. Associated with late albite, late K-feldspar, and fluorite.
Հազվագյուտ հողային տարրերի (REEs) նոր ICP-MS անալիզների տվյալներով Թեժսարի և Մեղրու ալկալային կոմպլեքսների ապարները բնութագրվում են Ce-ային խմբի թեթև լանթանոիդների հատկապես` La-ի, Ce-ի և Nd-ի բարձր պարունակություններով, իսկ ծանր հազվագյուտ հողերից համեմատաբար բարձր պարունակություններ ունեն Y-ը և Gd-ը: Թեժսարի ալկալային կոմպլեքսի ապարները Մեղրու պլուտոնի համեմատությամբ ունեն REEs-ի համաչափորեն առավել բարձր պարունակություններ (ղեկ.՝ ե.գ.թ. Ս. Հովակիմյան):

## Slide 29
Potential of REEs and Li deposits related to the Tejsar alkaline complex
Li -bearing pegmatite of the Tejsar complex: 0.3 wt% Li
Meliksetian (1971); Sokoł et al. (2018)
The Tejsar nepheline syenite complex has been identified as a major source of REEs (lanthanides, Sc, and Y) and High Field Strength Elements (HFSE) (Zr, Hf, Ti, Nb, Ta) in Armenia. Other elements that have been reported include:
0.3 wt% Li
Chart: 
| La | Ce | Pr | Nd | Sm | Eu | Gd | Tb | Dy | Ho | Y | Er | Tm | Yb | Lu
Neph. Syenite | 66.396 | 38.552 | 23.2629 | 14.1068 | 6.1635 | 3.2186 | 3.1848 | 2.4612 | 2.0066 | 1.7644 | 2.0196 | 1.8283 | 1.8531 | 1.8718 | 1.8945
Neph. Syen. Pegmat. | 128.356 | 66.8893 | 33.5886 | 17.3534 | 6.7643 | 3.6412 | 3.6005 | 3.0627 | 2.8066 | 2.7911 | 3.16 | 3.1111 | 3.4079 | 3.4911 | 3.6
Neph. Syen. Pegmat. | 85.46 | 43.172 | 19.7917 | 9.2863 | 3.2281 | 1.8196 | 1.5109 | 1.2313 | 1.0659 | 0.98515 | 1.3893 | 1.064 | 1.2325 | 1.4344 | 1.5934
Neph. Syenite | 55.38 | 39.2747 | 27.6295 | 18.3945 | 9.1179 | 4.5392 | 4.6386 | 3.3925 | 2.5846 | 1.9485 | 1.8304 | 1.633 | 1.3355 | 1.1089 | 0.8967
Hambaryan et al. (in prep)
Notes: Հազվագյուտ հողային տարրերի (REEs) նոր ICP-MS անալիզների տվյալներով Թեժսարի և Մեղրու ալկալային կոմպլեքսների ապարները բնութագրվում են Ce-ային խմբի թեթև լանթանոիդների հատկապես` La-ի, Ce-ի և Nd-ի բարձր պարունակություններով, իսկ ծանր հազվագյուտ հողերից համեմատաբար բարձր պարունակություններ ունեն Y-ը և Gd-ը: Թեժսարի ալկալային կոմպլեքսի ապարները Մեղրու պլուտոնի համեմատությամբ ունեն REEs-ի համաչափորեն առավել բարձր պարունակություններ (ղեկ.՝ ե.գ.թ. Ս. Հովակիմյան):

## Slide 30
Lithium pegmatite grades range from 0.15% to 1.5% Li
John Sykes
MinEx Consulting 2019
Heuberger & Morgenthaler, 2023
Tonnage and grades of lithium pegmatites deposits
There are 55 lithium pegmatite resources globally

## Slide 31
Southern Armenian Block: Potential for alkaline silicate REE-HFSE & Li deposits related to Cenozoic mantle-dominated & K-rich magmatism
Meghri: Monzogabbro-Monzodiorite
37-38 Ma (Rezeau et al., 2016)
Spodumene-bearing pegmatite in Meghri complex
Li pegm.
Chemical analysis in the spodumene-bearing sample of pegmatite revealed Li (1.80%), Be (0.006%), Rb (0.16%). In addition, spectral analysis identified the following elements: Be (0.03%), Li (> 3%), Si, Al, Fe, Ca, Na (~ 1.0%), Sn, Ti, Mn (0.1%), Nb, Cu, Zn (0.03%).
Karamyan et al. 1974;
Rezeau et al. 2018
Hambaryan et al. (in prep)
Chart: 
| La | Ce | Pr | Nd | Sm | Eu | Gd | Tb | Dy | Ho | Y | Er | Tm | Yb | Lu
Fels. Pegmatite | 66.912 | 29.9 | 13.0076 | 5.9712 | 2.3232 | 1.2108 | 1.231 | 1.0284 | 0.91648 | 0.90495 | 1.135 | 1.0202 | 1.1776 | 1.3098 | 1.3055
Maf. Pegmatite | 37.012 | 25.1893 | 17.8318 | 13.1548 | 6.8631 | 4.7137 | 3.7554 | 2.4672 | 1.7451 | 1.3802 | 1.3254 | 1.1178 | 0.90351 | 0.77541 | 0.70549
Maf. Pegmatite | 26.504 | 20.0573 | 15.3242 | 12.1932 | 6.981 | 4.9069 | 4.0598 | 2.6448 | 1.9319 | 1.4881 | 1.4239 | 1.1953 | 0.95614 | 0.80492 | 0.71429
Fels. Pegmatite | 13.748 | 4.456 | 1.6386 | 0.78904 | 0.3384 | 0.50588 | 0.22011 | 0.24776 | 0.29011 | 0.3802 | 0.55607 | 0.56566 | 0.92105 | 1.3252 | 1.6813
Micropegmatite | 3.9 | 2.9827 | 2.0553 | 1.3548 | 0.68441 | 0.31667 | 0.52717 | 0.50448 | 0.46593 | 0.47228 | 0.50321 | 0.52862 | 0.53289 | 0.54951 | 0.52747
Alk. Syenite | 39.604 | 26.5787 | 17.3917 | 11.2164 | 5.2129 | 3.3618 | 2.6766 | 1.906 | 1.4418 | 1.1515 | 1.1514 | 0.9798 | 0.87061 | 0.7718 | 0.67692
Fels. Pegmatite | 31.912 | 16.464 | 8.1803 | 4.2055 | 1.4601 | 0.80588 | 0.66848 | 0.47313 | 0.38022 | 0.33762 | 0.38929 | 0.31987 | 0.32456 | 0.34918 | 0.37802
Alyer. Rock | 40.708 | 25.8173 | 16.7992 | 11.6411 | 5.8783 | 3.9029 | 3.2201 | 2.0836 | 1.5626 | 1.2317 | 1.2146 | 1.0572 | 0.89474 | 0.80721 | 0.72527
Notes: Հազվագյուտ հողային տարրերի (REEs) նոր ICP-MS անալիզների տվյալներով Թեժսարի և Մեղրու ալկալային կոմպլեքսների ապարները բնութագրվում են Ce-ային խմբի թեթև լանթանոիդների հատկապես` La-ի, Ce-ի և Nd-ի բարձր պարունակություններով, իսկ ծանր հազվագյուտ հողերից համեմատաբար բարձր պարունակություններ ունեն Y-ը և Gd-ը: Թեժսարի ալկալային կոմպլեքսի ապարները Մեղրու պլուտոնի համեմատությամբ ունեն REEs-ի համաչափորեն առավել բարձր պարունակություններ (ղեկ.՝ ե.գ.թ. Ս. Հովակիմյան):

## Slide 32
Pegmatites of the Meghri pluton

## Slide 33
Zinnwaldite- and tourmaline-bearing rocks, Elba Island, Italy
Li- micas (Zinnwaldite) and tourmaline orbicules (schorl- elbaite)

## Slide 34
From Rezeau at el. 2017, based on the Karamyan et al. 1974
Tourmaline-bearing rocks of Vank-Kaler, Meghri pluton, south Armenia: Li 0.1-0.3%; Ga 0.03-0.1%; Sr 0.1-0.3%; Be 0.01-0.03%; as well as La, Cu, Mo, Sn, Ni, Co, V (Meliksetyan B.M, 1986).
Tourmaline-bearing rocks of Vank-Kaler, Meghri pluton։ any lithium potential?

## Slide 35
Mine site name | Re g/t | Estimated t Re | Data sources
Kadjaran | 0.26 | 500 | Website 2016- 05-01; John et al. (2017)
Teghout | 0.10 | 44 | Website 2016- 06-02
Agarak | 0.34 | 40 | Singer et al. (2008); Berzina et al. (2005); John and Taylor (2016); Barton et al. (2020)
Dastakert | 0.17 | 6 | Sinclair et al. (2016)
Chile (50.4 %)
Armenia (0.44 %)
China (4.2 %)
Kazakhstan
(0.84%)
Korea (4.7%)
U.S.A.
(15.6 %)
Poland
(15.6 %)
Uzbekistan
(8.2 %)
USGS (2023)
High Re potential of porphyry Cu-Mo deposits in Armenia
The average Re concentrations in molybdenites of porphyry Cu-Mo deposits
Re world production 2021:
59.5 tons
Chart: Re %
| Քեֆաշեն | Դաստակերտ | Հանքավան | Ագարակ | Քաջարան | Կապուտջուղ | Լիճք | Այգեձոր | Պռոշիբերդ | Ելփին | Վարդենիս
 | 0.0095 | 0.022 | 0.0244 | 0.038 | 0.04 | 0.0425 | 0.0971 | 0.1075 | 0.43 | 0.45 | 1.66
Kadjaran
Agarak
Lichk
Aygedzor
Kefashen
Yelpin
Vardenis
Dastakert
Hanqavan
Kaputjugh
Proshiberd
Simonyan (PhD thesis; in progress)
Kadjaran
Agarak

## Slide 36
Critical minerals in epithermal gold systems
WNW
SW
Eocene Meghradzor deposit
NE
Mid Eocene Sotk epithermal Au deposit
SWS
ENE
Se, Te, Bi, Cd, In, Ga, Ge
modified from Mederer et al. 2014
Au–Ag-telluride, including krennerite (AuTe2), sylvanite (AuAgTe4), petzite (Ag3AuTe2) and hessite (Ag2Te), altaite (PbTe), and native tellurium
Notes: Tellurides are part of the mineral paragenesis in the Jurassic Shahumyan deposit in the Kapan mining district
Indium (0.008%), gallium (0.01%), cadmium (1%), and germanium (0.003%) have been reported in sphalerite (Maghakyan et al. 1972).

## Slide 37
Shahumyan 12.4 Mt @
0.56 % Cu - 2.5 % Zn
2.5 g/t Au - 50 g/t Ag
Mederer et al. (2014, Ore Geol Rev)
Au–Ag-telluride, including krennerite (AuTe2), sylvanite (AuAgTe4), petzite (Ag3AuTe2) and hessite (Ag2Te), altaite (PbTe), and native tellurium
Indium (0.008%), gallium (0.01%), cadmium (1%), and germanium (0.003%) have been reported in sphalerite
Tellurides are part of the mineral paragenesis in the Jurassic Shahumyan deposit in the Kapan mining district
Critical minerals in epithermal gold systems

## Slide 38
The Abovyan Kiruna-type IOA deposit: Potential for REEs
The Abovyan-Kaputan magnetite- apatite deposit is interpreted as a Kiruna -type deposit
Gutanasar volcano
W
E
Pleistocene volcanic cover rocks
Abovyan-Kaputan is a blind deposit explored by drilling
Nekrylov et al. 2025
Massive magnetite outcrop near Kaputan village;
Massive magnetite-apatite ore;
White apatite in voids within massive magnetite;
Breccia type ore with magnetite in the matrix of the breccia.

## Slide 39
The Abovyan Kiruna-type IOA deposit: Potential for REEs
Spectra of REE+Y for Abovyan’s apatite from massive iron ore in comparison with apatite from El Laco, Kiruna and Bafq districts (Nekrylov et al. 2025).
The Abovyan deposit is characterized by significantly high REE concentrations.
The deposit's REE enrichment is primarily associated with apatite, where REE+Y concentrations reach up to 3 wt%, and averaging 2 wt%, with predominance of LREE, such as cerium (Ce), lanthanum (La), neodymium (Nd), and praseodymium (Pr).
The total REE+Y resources were estimated ~127 kt.
This allows to consider the Abovyan deposit as a significant regional source of REE+Y, particularly LREE, hosted primarily in apatite.

## Slide 40
Concluding remarks
Potential for critical & rare metals in Armenia still remains largely underexplored and requires future investigations /exploration.
Cenozoic alkaline magmatic complexes in the SAB, including nepheline syenite represent promising targets for exploration of critical metals, in particular Rare Earth Elements (REE).
Pegmatites of the Tejsar alkaline complex and the Meghri pluton represent prospective hosts for lithium (Li) mineralization.
Epithermal Au and base metal systems show a high potential for tellurium (Te) enrichment.
Cenozoic porphyry Cu–Mo deposits of the South Armenian Block are recognized as important sources of rhenium (Re).
Potential for REE in Kiruna-type magnetite-apatite deposit (Kaputan/ Abovyan).

## Slide 41
Main produced host metals and their by-products
Jébrak, 2015

## Slide 42
Thank you for your attention
«22IRF‐08» Critical Metals Research Project (CMRP)
Incoming Research Fellowship Program 2022

## Slide 43
Laboratory facilities
Al, Si, K, Ca, S, P, Cl, Ti, V,Cr, Mn, Fe, Co, Ni, Cu, W, Zn, Hg, As, Pb, Bi, Se, Th, U, Rb, Sr, Y, Zr, Nb, Mo, Ag, Cd, Sn, Sb La, Ce, Nd, Pr, Ba, Au, Re, Te

## Slide 44
Dr. Samvel
Hovakimyan
Dr. Nikolay
Nekrilov
MSc. Karen Hambaryan
MSc. Manya
Simonyan
Ruzanna
Serobyan
Prof. Robert Moritz
University of Geneva, Switzerland
Critical Minerals Research Group
Post-doc
PhD student
PhD student
BSc student
Principal Investigator
Project foreign collaborators
Dr. Christian Bergemann
University of Heidelberg, Germany